## Slide 1
EEE429 Final Project
Mid-Term Progress Presentation
MNIST CNN — Quantization-Aware Training & HW Artifact Generation
Based on: EEE426_FINAL.ipynb
Notes: Good morning. This is our mid-term progress report for EEE429. We will walk through exactly what we have completed so far — the quantized CNN model, training results, and all hardware artifact exports — as implemented in EEE426_FINAL.ipynb.

## Slide 2
What We Have Completed
EEE426_FINAL.ipynb — full software pipeline end-to-end
①
Quantization Scheme
ap_fixed<16,7> emulated in PyTorch with clamp + round
②
Quantized CNN Model
QUANTIZED_MNISTCNN — full 3-Conv + Pool + FC, QAT throughout
③
Training & Evaluation
5 epochs · Adam · batch 256 · test acc peaked at 98.92%
④
Best Checkpoint
QUANTIZED_MNISTCNN-2026-05-19-00-18-25.pth · full-set acc 99.36%
⑤
weights.h Export
All 8 tensors snapped to fixed-point grid, timestamped C header
⑥
images.h Export
280 images, shape [280][1][28][28], float C header
⑦
MNIST .npy Generation
70 k images + labels digit-sorted, ready for co-sim
Notes: This slide summarises all completed deliverables. Every item listed has been executed and outputs verified inside the notebook. I will go through each in detail on the following slides.

## Slide 3
CNN Architecture
Spec-compliant topology — unchanged from project brief
Input 1×28×28
→
Conv1 1→16, k=3 →16×26×26
→
Conv2 16→32, k=3 →32×24×24
→
Conv3 32→32, k=3 →32×22×22
→
MaxPool 2×2 →32×11×11
→
Flatten 3 872
→
FC 3872→10
→
Output Label
Q
Q
Q
Q
Q
Q = FixedPointQuantize inserted before ReLU at each layer output + after pool
Layer | Class | In → Out channels | Kernel / Stride | Output shape | Bias
Conv1 | QuantizedConv2d | 1 → 16 | 3×3 / 1 | 16 × 26 × 26 | ✓
Conv2 | QuantizedConv2d | 16 → 32 | 3×3 / 1 | 32 × 24 × 24 | ✓
Conv3 | QuantizedConv2d | 32 → 32 | 3×3 / 1 | 32 × 22 × 22 | ✓
MaxPool | nn.MaxPool2d | — | 2×2 | 32 × 11 × 11 | —
FC | QuantizedLinear | 3 872 → 10 | — | 10 | ✓
Notes: The architecture is fixed by the project spec. All three convolutional layers use valid-padding three-by-three kernels, stride one. The spatial dimension steps from twenty-eight to twenty-six to twenty-four to twenty-two. After the two-by-two max pool we get eleven by eleven by thirty-two, which flattens to 3872. The FC layer maps that to ten class scores. Red Q badges show where a fixed-point quantizer is inserted in the forward pass.

## Slide 4
Fixed-Point Scheme: ap_fixed⟨16, 7⟩
Emulated in Python; identical semantics to Vivado HLS ap_fixed
Word width W
16 bits
Integer bits I
7 bits (includes sign)
Fraction bits F
9 bits (= W − I)
Scale factor
2⁹ = 512
Min value
−64
Max value
64 − 2⁻⁹ ≈ 63.998
Quantum / LSB
2⁻⁹ ≈ 0.00195
16-bit word layout
S
5
4
3
2
1
0
-1
-2
-3
-4
-5
-6
-7
-8
-9
← Integer (7 bits, incl. sign) →
← Fraction (9 bits) →
def fixed_point_round(x): x = torch.clamp(x, -64, 64 - 2⁻⁹) x = torch.round(x * 512) / 512 return x # STE backward def backward(ctx, grad): return grad # pass-through
Notes: We use sixteen-bit signed fixed-point with seven integer bits and nine fraction bits. The representable range is minus sixty-four to roughly plus sixty-four. In Python the emulator clamps the tensor to that range and rounds to the nearest 1/512. Importantly the backward pass uses a straight-through estimator — the gradient passes through the quantizer unchanged so training stays stable. The exported C header declares using fixed_t equal to ap_fixed sixteen seven AP_RND AP_SAT which is bitwise identical to this emulation.

## Slide 5
QAT Forward Graph
Exact quantization insertion order from QUANTIZED_MNISTCNN.forward()
INPUT x — Normalize(0.5, 0.5) → range [−1, +1]
Q(x) — FixedPointQuantize — input quantization
QuantizedConv2d 1 — q_w = Q(self.weight), q_b = Q(self.bias)
Q(conv1 out) — FixedPointQuantize — before ReLU
ReLU — in-place clamp ≥ 0
QuantizedConv2d 2 — same pattern
Q(conv2 out) — FixedPointQuantize
ReLU
QuantizedConv2d 3
Q(conv3 out) — FixedPointQuantize
ReLU
MaxPool2d(2) — kernel 2×2
Q(pool out) — FixedPointQuantize — after pool
Flatten → FC — QuantizedLinear(3872→10)
Logits — CrossEntropyLoss during training
Notes: This is the exact forward pass order in the notebook. The input is first snapped to the fixed-point grid. Then for each convolution we quantize weights and biases inside QuantizedConv2d, quantize the convolution output, and then apply ReLU. After the third convolution and ReLU the pooled output is quantized one more time. Finally the flattened vector goes through QuantizedLinear which also quantizes its weights. The HLS kernel must mirror this order exactly.

## Slide 6
Training Setup
Hyperparameters and environment — from notebook cells
Parameter | Value
Framework | PyTorch + torchvision (Colab, T4 GPU)
Model class | QUANTIZED_MNISTCNN
Optimizer | Adam
Learning rate | 1 × 10⁻³
Batch size | 256
Epochs | 5
Loss function | CrossEntropyLoss
Input preprocessing | ToTensor + Normalize(mean=0.5, std=0.5) → [−1, +1]
Data split | train: 60 000 test: 10 000 total eval: 70 000
Checkpoint saves | Best test accuracy (each epoch saved if improved)
Notes: Training ran on Google Colab with a T4 GPU. We used Adam with one-thousandth learning rate, batch size two fifty-six, and five epochs. Best checkpoint is saved to milestones. Input preprocessing normalises pixel values from zero-one to minus-one to plus-one. This same transform must be applied on the board driver at inference time.

## Slide 7
Training Results — Epoch Log
QUANTIZED_MNISTCNN · 5 epochs · Adam lr=1e-3 · batch=256
Epoch | Train Acc | Train Loss | Test Acc | Test Loss | Saved?
0 | 91.69 % | 0.29000 | 97.97 % | 0.06443 | ✓ *
1 | 98.16 % | 0.06245 | 98.44 % | 0.04900 | ✓ *
2 | 98.62 % | 0.04626 | 98.69 % | 0.04052 | ✓ *
3 | 98.87 % | 0.03645 | 98.64 % | 0.03848 | —
4 | 99.05 % | 0.03035 | 98.92 % | 0.03147 | ✓ * ← best
Full-dataset evaluation (train + test = 70 000 samples)
Checkpoint filename | Full-set Accuracy
QUANTIZED_MNISTCNN-2026-05-19-00-18-25.pth (latest) | 99.36 %
QUANTIZED_MNISTCNN-2026-05-17-23-48-02.pth (previous) | 99.10 %
Notes: Looking at the epoch log: training accuracy climbs from ninety-one percent to ninety-nine percent over five epochs. Test accuracy peaked at ninety-eight point ninety-two percent on epoch four, which triggered a checkpoint save. The full-dataset number of ninety-nine point thirty-six percent is higher because the model was also evaluated on its own training data. The key number for the course is the test accuracy of ninety-eight point ninety-two percent which is well above the ninety-three percent threshold.

## Slide 8
WeightEmbed — weights.h Export
Checkpoint class → ap_fixed C header, auto-timestamped
Load .pth
torch.load(path, map_location='cpu')
Iterate state_dict
keys: conv1.weight / .bias … fc.weight / .bias
fixed_point_round_tensor
clamp → round to 1/512 grid
_nested_format
Recursively build C brace-initialiser string
Write .h
using fixed_t = ap_fixed<16,7,AP_RND,AP_SAT>
Tensor key | Shape | Total params
conv1.weight | (16, 1, 3, 3) | 144
conv1.bias | (16,) | 16
conv2.weight | (32, 16, 3, 3) | 4 608
conv2.bias | (32,) | 32
conv3.weight | (32, 32, 3, 3) | 9 216
conv3.bias | (32,) | 32
fc.weight | (10, 3872) | 38 720
fc.bias | (10,) | 10
Total | — | 52 778
Output: weights_YYYY-MM-DD-HH-MM-SS.h · Latest: weights_2026-05-19-00-21-15.h (7 983 lines)
Notes: The Checkpoint class loads the PyTorch state dictionary and iterates over every tensor. Each tensor is snapped to the sixteen-seven fixed-point grid using the same clamp-round function as training. It then generates a nested C brace initialiser and writes one self-contained header file. The file declares a using typedef matching the HLS ap_fixed type so the hardware C code can include it directly. Shape defines such as CONV1_WEIGHT_DIM0 and so on are emitted for each tensor so the HLS kernel can reference them symbolically. The latest output file is about eight thousand lines long.

## Slide 9
ImageEmbed — images.h & MNIST NumPy Export
Test vectors for HLS co-simulation and hardware bring-up
images.h
• 280 sample images, 28 per digit (digits 0–9)
• Shape: [280][1][28][28] — NOT flattened
• dtype: float (same Normalize(0.5, 0.5) as training)
• Format: static const float IMAGES[280][1][28][28] = {…}
• #define IMAGE_NUM 280
MNIST_DATASET_*.npy
• Full 70 000 images + labels
• Sorted by digit: 0×7000, 1×7000 … 9×7000
• IMAGE shape: (70000, 1, 28, 28) — preserves CHW
• LABEL shape: (70000,) int64
• Used for RTL/HLS co-simulation ground truth
Export calls (from notebook):
mnist.export_h(280, "float", lambda x: f"{repr(x)}f", "./images.h") mnist.export_np("./MNIST_DATASET_IMAGE.npy", mode="image") mnist.export_np("./MNIST_DATASET_LABEL.npy", mode="label")
Note: MNIST data is digit-bucketed, then interleaved 28 samples per digit for images.h
Notes: The image export section produces two types of output. images.h contains two hundred eighty hand-picked samples — twenty-eight per digit — in a four-dimensional C array. Shape is preserved as batch by channel by height by width. This allows the hardware team to compile a quick functional test without extra infrastructure. The NumPy exports cover all seventy thousand MNIST images sorted by digit class, which is convenient for co-simulation where you want to sweep a full digit at a time.

## Slide 10
Complete Software Pipeline
EEE426_FINAL.ipynb — end-to-end flow
DATASET
MNIST 70k ToTensor + Normalize(0.5,0.5)
→
QAT MODEL
QUANTIZED_MNISTCNN ap_fixed<16,7> throughout
→
TRAINING
Adam, lr=1e-3 batch 256, 5 epochs
→
BEST CKPT
QUANTIZED_MNISTCNN- 2026-05-19-00-18-25.pth
→
weights.h
8 tensors, C header ap_fixed<16,7,AP_RND,AP_SAT>
→
images.h
280 images [280][1][28][28] float
→
MNIST .npy
IMAGE (70k,1,28,28) LABEL (70k,) int64
Test: 98.92 % Full-set: 99.36 %
SW output for hardware team →
All outputs verified and committed. Ready to hand off to hardware team.
Notes: This diagram shows the full software pipeline as it stands today. Starting from MNIST data we train QUANTIZED_MNISTCNN with QAT. The best checkpoint at ninety-eight point ninety-two percent test accuracy is saved. From that checkpoint we export a weights.h file containing all eight tensors snapped to the fixed-point grid, plus images.h and NumPy archives for co-simulation. Everything to the right of the dotted line is an artifact consumed by the hardware team.

## Slide 11
Remaining Work & Interface Contract
What still needs to be agreed / implemented
Hardware (in progress)
• HLS kernel implementing exact forward graph (conv→Q→relu order)
• DMA / Overlay integration on Pynq-Z2
• Bitstream (.bit) + hardware handoff (.hwh)
• C-sim / Co-sim reports using exported weights.h + images.h
Joint agreement needed
• Confirm tensor memory layout with HW team: weight order [out_ch, in_ch, kH, kW]
• Agree on board input format: same Normalize(0.5, 0.5) as training
• On-board accuracy measurement vs 98.92 % SW baseline
• Runtime measurement: only preprocessing + kernel loop + accumulation
SW remaining
• Pynq board driver notebook (numpy / pynq only — course rule)
• Final accuracy vs runtime comparison table for report
Notes: On the hardware side the team is implementing the HLS kernel to match our forward graph order. The most important joint agreement is that the memory layout of each tensor and the input normalisation must exactly match. On the software side I still need to write the board-side Jupyter notebook driver using only NumPy and PYNQ as required by the course. After the bitstream is available we measure inference accuracy and runtime on the board and compare against our ninety-eight point ninety-two percent software baseline.

## Slide 12
Thank You
Questions?
Checkpoint: QUANTIZED_MNISTCNN-2026-05-19-00-18-25.pth | Test acc: 98.92 % | Full-set: 99.36 %
Notes: Thank you. I am happy to take questions on the quantization scheme, the exact forward-pass order, the export format, or the interface contract with the hardware team.